## Slide 1: CS425 Introduction to Frequency analysis – Part II

## Slide 2: Back to the Fourier Transform
Next we’ll just consider how the Fourier transform is a measure of similarity
Essentially, by taking the Fourier transform you are measuring the similarity between the waveform f(t) and each of the waves cos(wt) and sin(wt) at the frequency w
More similarity with these would imply more energy at that frequency w

## Slide 3: Fourier link with Correlation (Similarity)
Correlation is a a technique from statistics used to measure the similarity between two time series
High correlation value means greater similarity

## Slide 4: Correlation Equation
In essence it is a multiplication followed by an integration
Consider when s=0 the two time series are aligned

## Slide 5: Fourier Transform and Correlation
Thus, our Fourier transform is like a correlation between f(t) and g(t)=ejwt
Thus, the Fourier transform is essentially measuring the similarity between the signal f(t) and the complex exponential signal at frequency w which is made from a cosine and a sine

## Slide 6: Example – high correlation

## Slide 7: Example – low correlation

## Slide 8: The continuous time Fourier Transform equation
The continuous-time Fourier transform is given by

## Slide 9
𝑓(𝑥) - the signal which we want to analyze
𝜉 - the transform frequency
𝑖 - Imaginary number
𝑒 – Euler constant

## Slide 10
Resources for Fourier transform:
https://www.youtube.com/watch?v=spUNpyF58BY
https://www.youtube.com/watch?v=r18Gi8lSkfM
https://www.youtube.com/watch?v=kK2nIz0R8eA
To understand and visualize Euler's formula:
https://www.youtube.com/watch?v=E_1APPC7lqA
https://www.youtube.com/watch?v=n-tlWztL7C8

## Slide 11: Frequency Spectrum
If we measure the similarity between the signal f(t) and many different values for the cosines and sines at frequency w then we have what is known as the frequency spectrum
How to choose values of w at which to measure?
The most common approach is to pick values of the frequency w that are uniformly spaced across the frequency axis

## Slide 12: Frequency Spectrum
Because the exponential is complex valued (i.e. has a real and imaginary part) then the spectrum F(w) is a complex number
Thus, we need some further processing to find the magnitude of the spectrum and the phase of the spectrum

## Slide 13: Frequency Spectrum
Magnitude: find the absolute value of F(w)
Phase: find =tan-1(Imaginary (F(w))/Real (F(w))

## Slide 14: Phase Spectrum
=tan-1(Imaginary (F(w))/Real (F(w))

## Slide 15: Frequency Spectrum
Most of the time we are interested in looking at the magnitude spectrum rather than the phase spectrum
This is because the size of any frequency component in a signal determines whether we can hear it or not

## Slide 16: Frequency spectrum of a sinusoid
Sinusoid – frequency=20Hz; Sampling frequency =1000Hz

## Slide 17: Given a harmonic signal
x=sin(2.*pi.*fhz.*time)
+0.5.*sin(2.*pi.*2.*fhz.*time)
+2.*sin(2.*pi.*3.*fhz.*time)
+0.25.*sin(2.*pi.*6.*fhz.*time);
Where fhz=20Hz

## Slide 18: Frequency spectrum of a harmonic signal made from sinusoids

## Slide 19: Positive and Negative Frequencies
This is explained by the use of complex exponentials and Euler’s Formula
Euler’s formula for a sinusoid is
Euler’s formula for a cosine is

## Slide 20: Frequency Spectra – Sinusoid – positive and negative frequencies

## Slide 21: Frequency Spectra – Cosine – positive and negative frequencies

## Slide 22: The DFT equation
The discrete Fourier transform is given by

## Slide 23: Connecting the two
The integral of the continuous Fourier transform is equivalent to using the summation in discrete Fourier transform.
It is an implementation of the trapezoidal rule a well-known technique for approximating continuous integrals.

## Slide 24: Time and Frequency variables
In the continuous Fourier transform the time and frequency variables are t and w, which have units of seconds and radians respectively.
In the discrete version these quantities are given by n, the sample index, and k, the frequency bin index.

## Slide 25: Including the sampling frequency
To establish the connection between these indices and their physical meaning the discrete equation can be rewritten using the sampling frequency Fs, and the sampling period Ts,

## Slide 26: Rewriting the DFT equation

## Slide 27: Interpretation
Because Ts=1/Fs, they cancel and do not effect the outcome of the equation.
Now the discrete Fourier transform can be interpreted as an evaluation of the frequency content of the sampled signal x[n] that exists at discrete time instances given by nTs

## Slide 28: Interpretation
This signal has N discrete frequency components at locations (2pk/N)Fs where k=0,…., N-1
The magnitude and phases of these components are found by evaluating X[k] for k=0,…., N-1

## Slide 29: Applying the DFT
We can program the DFT directly but it can be very slow because there is a nested loop to compute
The FFT algorithm was invented to speed up the computation but is only fast when the signal length is a power of two

## Slide 30
Resources for Discrete Fourier transform:
https://www.youtube.com/watch?v=mkGsMWi_j4Q&t=4s
https://www.youtube.com/watch?v=yYEMxqreA10&t=3s