## Slide 1: CS425 Introduction to Frequency analysis – Part III

## Slide 2: DFT Examples – Digital Cosine Spectrum

## Slide 3: In the dB domain – 20*log10()

## Slide 4: Scale by the length of the transform 32768

## Slide 5: Scale by the length of the transform 32768
Peak magnitude is 0dB

## Slide 6: Do the same for a sinewave of frequency 1024Hz

## Slide 7: Do the same for a sinewave of frequency 1024Hz

## Slide 8: The Digital Spectrum is Infinite
The spectrum of this cosine extends to infinity
….. inf
–inf…

## Slide 9: Digital Spectrum
Normally the spectrum is plotted up to Fs/2 but it actually is infinite with repetitions of the spectral information from 0 to Fs/2
The important implication is to remember that actual digital signals are not bandlimited

## Slide 10: Component Frequency and Bin frequency do not coincide
If the frequency of the cosine wave is 1024.5Hz then the component does not sit exactly on a frequency bin. This will change the appearance of the frequency spectrum

## Slide 11: Cosine frequency 1024.5Hz

## Slide 12: Cosine frequency 1024.5Hz

## Slide 13: Why the change?
This change in appearance is because the signal under analysis being input to the FFT has an incomplete period
Comparing the two signals it is clear that the end of the 1024Hz signal can connect correctly to its beginning meaning that it has no incomplete periods while for the 1024.5Hz signal this is not true

## Slide 14: Compare the two signals 1024Hz
The end of this signal fits perfectly to the start of this

## Slide 15: Compare the two signals 1024.5Hz
The end of this signal does not fit perfectly to the start of this

## Slide 16: Windowing
This can also be explained by the theory of windowing
A window is essentially looking at a possibly infinite signal through a reduced aperture
In the previous cases we have a rectangular window

## Slide 17: Different Windows

## Slide 18: In the Frequency Domain

## Slide 19: Time and Frequency
Looking at the signal through a window effectively means multiplying the signal by the window in time
This changes the shape of the signal
This changes the spectrum of the signal and the new spectrum is the convolution of the signal spectrum with the spectrum of the window

## Slide 20: Windows
Windows are applied a lot in signal analysis to smooth out any discontinuities at the ends of signals when we are computing the spectrum
It may not seem to be important with sinusoids but with real-world signals taking the FFT without windowing can result in lots of spurious spectral components (‘junk’) in the representation

## Slide 21: Part of a guitar note waveform

## Slide 22: Apply a Rectangular window

## Slide 23: Spectrum of Rectangular windowed section

## Slide 24: Apply a Hanning window

## Slide 25: Spectrum of Hanning windowed section

## Slide 26: Apply a Kaiser window

## Slide 27: Spectrum of Kaiser windowed section

## Slide 28: Window effects
Note that with the rectangular window you can obtain sharp peaks but lots of spectral junk at the base of those peaks
With the more half-cosine windows you get broader peaks but the magnitudes of the junk components are much lower down

## Slide 29: Another example of Window Effects on peak appearance

## Slide 30: Zero Padding
This is a technique used to gain a better plot from the FFT – often used to bring the length of the signal data for analysis to be a power of two for faster processing
The magnitude output from the FFT is smoother in appearance
In the strictest sense it does not provide better frequency resolution

## Slide 31: Zero padding Example

## Slide 32: Example 2
There are two cosines at Frequencies 64 and 64.5Hz with a sampling frequency of 512Hz. Zero padding does not reveal the second cosine

## Slide 33: Spectrum analysis non-periodic signals
In most practical cases the signals we have are not periodic
Some signals may also be very long so the number of operations to compute the FFT would be prohibitive
It is best then to break such signals into small segments and analyse each one individually with an FFT

## Slide 34: Spectrogram outline

## Slide 35: Spectrogram Principle
Its operation principle is that the audio signal is first buffered into frames that are normally overlapping.
The frame sizes are often a power of two in length. The length would reflect the belief in the time duration for which the frequency content in the signal is stationary, for example 10 or 20ms.
The frames are also overlapping and a common choice for the overlap is half the length of the frame.
After this is windowing. The windowing is done to remove the discontinuities at the edges of the frames. The typical window is half-cosine in shape such as a hanning window.

## Slide 36: Spectrogram Principle
Zero-padding may then be done to improve the smoothness of the resulting spectrogram.
This is then sent to the FFT. Here, the square magnitude is computed followed by the log10 operation to convert into dB which displays the power at each frequency bin.
The succession of FFTs is then displayed as a depth map where regions of higher spectral information appear as a darker or lighter intensity in the image.

## Slide 37: Spectrogram
This 2-dimensional data set requires a three-dimensional graphic display
This is usually done by plotting contour plots or gray-scale images
The preferred form is the spectrogram where the gray level at the each point is proportional, where large values are black and small values are white

## Slide 38: The Spectrogram
The horizontal axis is time and the vertical axis is frequency
The minimum shift of the sliding window is one sample point
However, it is not always necessary to compute the spectrogram at every time instant especially is the spectral content of the signal is not changing rapidly over time

## Slide 39: Sliding the window - hopping
Instead it is possible to skip over some of the time instants without losing the basic shape of the spectrogram
This means that the sliding window is moved by more than one sample each time, this is called the hop size

## Slide 40: Window Hopping

## Slide 41: Window Functions
There are actually a number of different window functions available, with the Rectangular being a specific case
The properties of the different windows have an effect on how the information will be displayed on the spectrogram

## Slide 42: Connecting Windows and Filters
The DFT equation is
If we are windowing we can write it as
where n0 is the time point at which we window the signal

## Slide 43: Rectangular window
If we use a rectangular window its equation is

## Slide 44: Filter interpretation
We can interpret the equation as a filtering operation where the filter is given by the combination of the window and the Fourier complex exponentials. Note how it looks like a convolution…

## Slide 45: Filter Interpretation
The term
Describe a bandpass filter whose centre frequency is given by (k/N) Fs
The window w[m-n0] represents a low pass filter impulse response that is shifted in the spectrum to become a bandpass filter

## Slide 46: The Lowpass Spectrum of a Rectangular Window

## Slide 47: Bandpass filter interpretation
The spectra of a number of rectangular windows behaving as bandpass filters

## Slide 48: Rectangular window
In the case of the Rectangular window its spectrum is wider than the width of each frequency component being measured leading to leakage from other frequency components present in the signal into the calculation
This means that the accuracy of our spectral representation is compromised

## Slide 49: Different Windows
To overcome the problems with the rectangular window, efforts have been directed towards designing windows that taper at the ends to give a more gentle weighting on the data
One well-known and commonly used window is the Hanning window

## Slide 50: Different Windows
Another window used widely is the Hamming window
For the Hamming window, its sidelobes are much lower than those of the rectangular window. However, the compromise is that the central lobe of the main window is broader, about twice as wide. This is the compromise in choosing a window

## Slide 51: Spectrogram Parameters
Two parameters are involved in the calculation of the spectrogram
1. The window length L
2. The number of analysis frequencies N (i.e. zero padding)
Its resolution performance is assessed in frequency and time. Resolution can be measured by determining its performance when processing two closely spaced components, either in frequency or time

## Slide 52: Window Length
The length of the window determines the width of its passband, and thus, impacts the frequency resolution
The hanning window has a passband width that is approximately equal to 2p4/L
However, if L is large, then the time resolution suffers and Short-duration time events or time transitions are lost when combined together by a long window

## Slide 53: Short and Long Window Spectra
The Spectra of Short and Long Windows
Short=blue line
Long= red line

## Slide 54: Time/Frequency Resolution trade-off
Good time resolution and good frequency resolution cannot be obtained simultaneously in the spectrogram
This is called the uncertainty principle and is equivalent to the Heisenberg principle in physics

## Slide 55: Sinusoid Example
The test signal is comprised of two components:
A 960Hz tone that persists over the entire data set and a 1000Hz tone whose beginning and ending times are 100 and 400msec respectively
Using a Hanning window,

## Slide 56: Sinusoid Example
The time resolution is directly proportional to the length of the window
The trade-off between time and frequency resolution can be seen for the cases L=512 and L=128

## Slide 57: Predicted Resolutions

## Slide 58: Short and Long Window Resolution
The frequency resolution of the longer window (L=512) is adequate to resolve the two signals, but it causes a blurring of the signals endpoints, which inhibits an accurate calculation of the starting and ending times
The shorter window (L=128) does find the ends of the signal but fails to resolve the two frequencies

## Slide 59: Good Frequency Resolution

## Slide 60: Good Time Resolution

## Slide 61: The Spectrogram for Speech
Choice of window length:
Narrow band analysis: resolves harmonics but blurs temporal detail such as burst onsets.
Wide band analysis: resolves fine temporal detail but looses fine frequency detail.
In most applications this tradeoff is manifested as the choice of window size. Good rule of thumb is to include a few pitch periods, say 20ms to 32ms.

## Slide 62: Speech Waveform

## Slide 63: Short Window - Good time Resolution
Formants visible but no harmonics

## Slide 64: In Detail

## Slide 65: Long Window - Good Frequency Resolution
Smearing exists at the beginning and end of events

## Slide 66: In Detail

## Slide 67: Heisenberg Uncertainty
Basically - we cannot know exactly what spectral components exist at what instances in time
One explanation is a tiling interpretation of the spectrogram where the shape of the tiles depict the region of uncertainty in the time-frequency plane regarding the frequency and location of a component.

## Slide 68: The Tiling Interpretation

## Slide 69
The Fast Fourier Transform
To evaluate all of the X[k] coefficients of the DFT, we need N multiplies and N-1 additions
The FFT provides a means of evaluating the DFT and IDFT equations with a number of operations proportional to N log2N
rather than N2
This behaviour becomes increasingly important for large values of N

## Slide 70
For example, if N=1024
The FFT will compute the coefficient set with 5120 complex multiplications
Direct evaluation of the DFT will result in 1,048,576 complex multiplications
The algorithm works best when N is a power of two. However, no savings are made if N is a prime number
The Fast Fourier Transform

## Slide 71: Convolution
A special mathematical operation that is well-known in signal processing
The signal y is the convolution of the signals x and h

## Slide 72: Example of Convolution
Consider the signals x[n]={2, 6, -1, -2} and h[n]={5, -3, 1}
n | 0 | 1 | 2 | 3 | 4 | 5
x[n] | 2 | 6 | -1 | -2 |  | 
h[n] | 5 | -3 | 1 |  |  | 
h[0] x[n-0] | 10 | 30 | -5 | -10 |  | 
h[1] x[n-1] |  | -6 | -18 | 3 | 6 | 
h[2] x[n-2] |  |  | 2 | 6 | -1 | -2
y[n] | 10 | 24 | -21 | -1 | 5 | -2

## Slide 73: More Detail
n | 0 | 1 | 2 | 3 | 4 | 5
x[n] | 2 | 6 | -1 | -2 |  | 
h[n] | 5 | -3 | 1 |  |  | 
h[0] x[n-0] | h[0] x[0] | h[0] x[1] | h[0] x[2] | h[0] x[3] |  | 
h[1] x[n-1] |  | h[1] x[0] | h[1] x[1] | h[1] x[2] | h[1] x[3] | 
h[2] x[n-2] |  |  | h[2] x[0] | h[2] x[1] | h[2] x[2] | h[2] x[3]
y[n] | 10 | 24 | -21 | -1 | 5 | -2

## Slide 74: Algorithm for Convolution
Draw a grid and then write out the n across the top where n=length(x)+length(h)-1, i.e. (4+3-1=6). n has 6 elements which means 0, 1,2 3, 4, 5.
You have a diagonal arrangement
First row is the h[0] by x[0] to x[3]
Second row is the h[1] by x[0] to x[3] (shifted by 1 relative to the first row)
Third row is the h[2] by x[0] to x[3] (shifted by 2 relative to the first row)
Add down the columns to get the final number.

## Slide 75: Convolution Operation
Sometime the Convolution operation is described as a folding and shifting
Convolution is used to describe the actions of filters on signals

## Slide 76: Convolution Example 1

## Slide 77: Convolution Example 2
Convolve the two sequences
X=[1 4 -2 5] and h=[ 1 -1 0.5 2.6]
Y=[1 3 -5.5 11.6 4.4 -2.7 13]

## Slide 78
Resources for Convolution:
https://www.youtube.com/watch?v=KuXjwB4LzSA&t=435s
https://www.youtube.com/watch?v=acAw5WGtzuk